## Slide 1: Taps, Dies and Threads
Mater Dei Robotics

## Slide 2: Agenda
Thread Types
Taps and Dies
How to Use
Mater Dei Robotics

## Slide 3: Thread Types
ISO Metric Screw Threads
  Maa x bb
    aa = Diameter in mm
    bb = Thread Pitch in mm
Unified Screw Threads
  Coarse or Fine
  Bolt Diameter and Threads per inch
    ¼-20 (UNC)
    ¼-28 (UNF)

## Slide 4: Taps and Dies
Taps used to thread holes.
Dies used to thread rods.

## Slide 5: How to Use
Apply a few drops of cutting fluid on tap and hole.
Insert tap lightly into hole, perpendicular to part.
Lightly rotate tap in clockwise/counterclockwise direction.
Continue until desired depth is tapped.